## Slide 1: IP Pie
Rednectar’s Guide to IP Subnetting using Pies

## Slide 2: Easy as Pie
Dividing IP networks into subnets is as easy as pie. All you need to do is remember one simple rule about how to cut the pie.
  Every time you make a cut, you must cut the piece of pie in HALF.

## Slide 3: C class pie
Here is an IP pie.
This is the /24 IP pie of a class C network and represents 256 addresses numbered 0 to 255.
  To illustrate the example, we will use the network 192.168.99.0
With no subnets, we can use the whole pie, which could supply us with 254 usable IP addresses.
255
192.168.99.0/24
0
/24

## Slide 4: C class pie
Lets cut the pie in half.
We now have two subnets, the 192.168.99.0 subnet and the 192.168.99.128 subnet
Each has a /25 mask and yields 126 usable host addresses
0
128
192.168.99.0/24
/25
/25

## Slide 5: C class pie
Lets cut the .0 piece in half.
This gives us the 192.168.99.0/26 and the 192.168.99.64/26 subnet
  Each of these subnets could have 62 hosts
The 192.168.99.128/25 subnet hasn’t changed, and could still accommodate126 hosts.
0
128
192.168.99.0/24
/25
/26
/26
64

## Slide 6: C class pie
Assume we have a WAN connection where we want to use as few IP addresses as possible.
  The smallest slice of pie we can allocate to a subnet is 4 IP addresses
We would have to start by slicing one of our /26 pieces in half.
  giving us two /27 slices, each yielding 30 addresses
0
128
192.168.99.0/24
/25
/26
/27
64
/27
96

## Slide 7: C class pie
Now divide one of the /27 slices into two
And one of the /28 pieces
And one of the /29 pieces
Our pie now has:
  2 x /30 subnets
  1 x /29 subnet
  1 x /28 subnet
  1 x /27 subnet
  1 x /26 subnet
  1 x /25 subnet
0
128
192.168.99.0/24
/25
/26
/27
64
/28
96
/30
/30
/29
112
120
124

## Slide 8: B class pie
The same principles apply to each octet of the IP address space.
For B class addresses, we could work with the /16 slice of pie, or the 3rd octet.
0
128
172.26.0.0/16
/17
/18
/19
64
/20
96
/22
/21
112
120
124
126
/23
/23

## Slide 9: Classless Pie
Each octet can be thought of as a pie.
/24
/16
/8
/0
/9
Every time you cut a pie, the mask gets 1 bit longer.
/9
0
128

## Slide 10: Classful Pie
Although the writers didn’t know it, they used IP pie to divide the IP address space into address classes
0
128
192
224
240
A
B
C
D

## Slide 11: Pie Problem Solving
Bill is having trouble connecting to server Alice. Can you spot the problem?
10.1.1.1/28
10.1.1.100/28
10.1.1.129/30
10.1.1.130/30
10.1.1.200/25
10.1.1.201/25
Bill
Alice
A
B

## Slide 12: Pie Problem Solving
Lets plot the IP addresses on an IP pie as shown in the diagram.
0
129
/30
100
10.1.1.0/24
201
200
1
130
10.1.1.1/28
10.1.1.100/28
10.1.1.129/30
10.1.1.130/30
10.1.1.200/25
10.1.1.201/25
Bill
Alice
A
B

## Slide 13: Pie Problem Solving
10.1.1.1/28
10.1.1.100/28
10.1.1.129/30
10.1.1.130/30
10.1.1.200/25
10.1.1.201/25
Bill
Alice
A
B
Lets plot the IP addresses on an IP pie as shown in the diagram.
Remember, all addresses on a common subnet must come from the same slice of pie
0
129
64
96
/30
112
100
128
10.1.1.0/24
201
200
1
/25
130
/28
/28

## Slide 14: Pie Problem Solving
10.1.1.1/28
10.1.1.100/28
10.1.1.129/30
10.1.1.130/30
10.1.1.200/25
10.1.1.201/25
Bill
Alice
A
B
This highlights two problems
Mismatched Subnets
  10.1.1.1 & .100 are not on the same /28 subnet
Overlapping Subnets
  10.1.1.200 & .201 are on the 10.1.1.128/25 subnet
  10.1.1.129 & .130 are on the 10.1.1.128/30 subnet
  These subnets overlap, indicating that whoever designed this network didn’t follow the rules of pie-cutting
0
129
64
96
/30
112
100
128
201
200
1
/25
130
/28
/28
10.1.1.0/24
Can’t cut off a /30 subnet without first cutting the /25 subnet in half etc
Not on same subnet
Not on same subnet

## Slide 15: Pie Problem Solving
A couple of possible solutions present themselves:
Solution 1
  Slice the pie properly, putting 10.1.1.200 & .201 on a /26 subnet, and
  Give 10.1.1.1 and 10.1.1.100 a /25 subnet slice
0
129
/30
100
128
201
200
1
/26
130
192
/25
10.1.1.0/24
10.1.1.1/25
10.1.1.100/25
10.1.1.129/30
10.1.1.130/30
10.1.1.200/26
10.1.1.201/26
Bill
Alice
A
B

## Slide 16: Pie Problem Solving
10.1.1.1/28
10.1.1.14/28
10.1.1.129/30
10.1.1.130/30
10.1.1.200/26
10.1.1.201/26
Bill
Alice
A
B
A couple of possible solutions present themselves:
Solution 2
  Slice the pie properly, putting 10.1.1.200 & .201 on a /26 subnet, and
  Move 10.1.1.100 to the same /28 subnet as 10.1.1.1
0
129
64
/30
128
201
200
1
/26
130
192
/28
14
10.1.1.0/24